## Slide 1: Heat of Combustion
Jonathan Gray
Galina Gheihman
Kent Phuong
Christopher Piggott
Bob Xue

## Slide 2: Introduction
Measuring change in heat energy during Combustion

## Slide 3: Combustion
Combustion is a chemical reaction:
Fuel + O2
CO2 + H2O

## Slide 4: Introduction
Heat absorbed or released
Endothermic vs. Exothermic
Heat change can be measured

## Slide 5: Calorimetry
An experimental technique
Calorific value:
The total amount of energy produced when 1 unit of mass of fuel is completely burnt.
Comparison of Efficiency

## Slide 6: Purpose of the Experiment
The purpose of the experiment is to ascertain which of three fuels is most efficient by using the experimental technique of calorimetry in determining the calorific value of each of the fuels, and then comparing these three values.

## Slide 7: Overview
Experimental Design
  Materials, Procedure
Observations
Calculations
  Percentage Yield, Percentage Error
Conclusion, Discussion
Sources of Error, Suggested Modifications

## Slide 8: Required Materials
Safety Goggles
Electric Scale
Calorimeter
Thermometer
Graduated Cylinder
50 mL of Water
Matches
Three Fuels:
Paraffin Wax
Cooking Oil
Butane

## Slide 9: The Calorimeter

## Slide 10: Procedure
50 mL of water was poured into the calorimeter.
The temperature of the water was measured and recorded.
1.
2.

## Slide 11: Procedure
Paraffin wax was obtained, measured, and placed into the calorimeter.

## Slide 12: Procedure
The paraffin wax was ignited and allowed to burn for at least 2 minutes, or until the flame went out.

## Slide 13: Procedure
The temperature of the water was measured again and recorded.
The paraffin wax was disposed of and the calorimeter's compartments were cleaned thoroughly.

## Slide 14: Procedure
The water was disposed of and replaced.
Steps 2 through 7 were repeated for cooking oil and butane.
The work area was cleaned and all equipment replaced.

## Slide 15: Safety
Safety goggles, appropriate clothing, hair tied back
Clear experiment area
Teacher present
Fire exits and procedures were known to all participants
Experiment area thoroughly cleaned upon completion
Refuse was disposed of accordingly

## Slide 16: The Experiment

## Slide 17: Observations
Fuel | Initial Temper- ature of Water (°C) | Final Temper-ature of water (°C) | Initial Mass of Fuel* (g) | Final Mass of Fuel* (g) | Δ Mass (g) | Δ Time (s)
Paraffin Wax | 22.5 | 25.6 | 16.963 | 16.877 | 0.086 | 134
Cooking Oil | 22.5 | 25 | 9.575 | 9.534 | 0.041 | 40
Butane | 22 | 39 | 210.443 | 210.170 | 0.273 | 120
*Includes container

## Slide 18: Calculations – Part 1
Calculating Mass of Fuel Burned (m)
= (initial mass) – (final mass) Paraffin Wax: 0.086 g Cooking Oil: 0.041 g
Butane: 0.273 g

## Slide 19: Calculations – Part 2
Calculating Difference in Temperature (Δt)
= (final temperature) – (initial temperature) Paraffin Wax: = 25.6°C – 22.5°C = 3.1°C Cooking Oil: = 25°C – 22.5°C = 2.5°C
Butane: = 39°C – 22°C = 17.0°C

## Slide 20: Calculations – Part 3
Calculating Heat Produced (Q) = (mass of water used) x (specific heat capacity of water) x (difference in temperature)
Paraffin Wax: = 50 x 4.18 x 3.1 = 647.9 J Cooking Oil: = 50 x 4.18 x 2.5 = 522.5 J
Butane: = 50 x 4.18 x 17 = 3553 J

## Slide 21: Calculations – Part 4
Calculating Calorific Value
= (heat produced) / (mass of fuel burned)
Paraffin Wax: = 7.53 kJ/g = 1.8 kcal
Cooking Oil: = 12.74 kJ/g = 3.05 kcal
Butane: = 13.01 kJ/g = 3.11 kcal

## Slide 22: Calculating Molar Calorific Value
Molar Calorific Value
= (heat produced) / (number of moles of fuel burned) = (heat produced) x (mass of fuel burned) / (molar mass of fuel)
Paraffin Wax = 0.158 J/mol Cooking Oil = 0.076 J/mol Butane = 16.689 J/mol

## Slide 23: Theoretical vs. Observed Values
Theoretical Calorific Values
Paraffin Wax: 46 kJg-1
Cooking Oil: 35 kJg-1
Butane: 49.5 kJg-1
Observed Calorific
Values
Paraffin Wax: 7.53 kJg-1
Cooking Oil: 12.74 kJg-1
Butane: 13.01 kJg-1

## Slide 24: Percentage Error
% Error = |(Theoretical Value - Experimental Value) / Theoretical Value| × 100%
Paraffin Wax % Error = |(46 - 7.53) / 46| x 100% = 83.63% Cooking Oil % Error = |(35 - 12.74) / 35| x 100% = 63.6% Butane % Error = |(49.5 - 13.01) / 49.5| x 100% = 73.7%

## Slide 25: Conclusion
Purpose: To determine the calorific value of 3 different fuels by using the techniques of calorimetry
Observations: Change in mass and the change in temperature used to calculate the calorific values of the fuels

## Slide 26: Conclusion
Calorimetry techniques can be used to measure and compare the combustion efficiency of a fuel against other fuels.
From the three fuels, butane is the most effective fuel.

## Slide 27: Discussion
Applications of Calorimetry:
Oil companies
  Testing efficiency of fuels
  Testing potential new fuels
Diet/Energy Intake
  Calories in food

## Slide 28: Sources of Error
Loss of Heat
    Lack of insulation
    Ventilation
    Gaps due to limited size
    Outside Ignition
Weighing of Fuels
    ~10% difference due to scale fluctuation
Incomplete combustion
    Lack of Oxygen
Lack of Bomb Calorimeter

## Slide 29: Bomb Calorimeter

## Slide 30: Suggested Modifications
Need for choosing appropriate fuels
Difficulties with combustion
Butane Lamp
  Size
  New Container
  Ventilation
Bomb Calorimeter
  Expensive
New Design
  Better insulation
  Ventilation at bottom
  Door at bottom
Digital Thermometer

## Slide 31: New Design

## Slide 32: Thank You